# 6502 Pin Compatible Variants

MOS/Rockwell/Synertek	6502	1 MHz
	6502A	2 MHz
	6502B	3 MHz
	6502C	4 MHz
Atari	Sally (6502C)	1.8 MHz
WDC	W65C02S	14 MHz

Ma			Pin1	Pin5	Pin34	Pin35	Pin36
6502			VSS (GND)	N.C.	R/W	N.C.	N.C.

Atari Sally			VSS (GND)	N.C.	N.C.	HALT	R/W
WDC65C02S			VPB	MLB	R/W	N.C.	BE

BE:	Bus Enable	input	When low A, D and R/W are high impedance (async)
HALT: Halt CPU	input	When low A, D and R/W are high impedance (async)
MLB:	Memory Lock	output	Low during memory read/modify/write cycles.
VPB:	Vector Pull	output	Low when CPU reads interrupt vector

WDC65C02:
RDY is bidirectional (low output during WAI instruction)